BIRDVIEW SKYLIGHTS

Technical Data:

Glass Glazing Options:

| Lighting / Solar Table for Standard Insulated Glass |
| --- |
| --- | Vis. Light Trans. | Solar Trans. |
| Clear | 87% | 71% |
| Bronze | 62% | 54% |
| Grey | 55% | 53% |
| For Comfort E (low E) |
| --- | Vis. Light Trans. | Solar Trans. |
| Clear | 77% | 66% |
| Bronze | 58% | 51% |
| Grey | 53% | 49% |

Acrylic Glazing Options:

| Lighting Table: Standard Colors |
| --- |
| Acrylic | Vis. Light Trans. | Solar Trans. |
| Clear | 92% | 85% |
| 2412 Bronze | 27% | 35% |
| 7328 White | 34% | 39% |
| (Many additional custom colors are available upon request.) |
| Non-standard Colors |
| Acrylic | Vis. Light Trans. | Solar Trans. |
| 2404 Bronze | 49% | 56% |
| 2370 Bronze | 10% | 20% |
| 2064 Grey | 27% | 44% |
| 2074 Grey | 13% | 32% |

Polycarbonate Glazing Options:

(based on 1/8" thick material)

| -- | Vis. Light Trans. | Solar Trans. |
| --- | --- | --- |
| Clear | 86% | 89% |
| Bronze | 27% | 35% |
| Grey | 50% | 60% |
| White | 56% | 56% |

Condensation:

Under certain conditions of high humidity and large temperature differentials, it is possible for condensation to occur on the metal and plastic surfaces. Double glazing will usually reduce the occurrence of condensation but will not totally eliminate it.

Note:

Due to the nature of plastic glazing material, noises from expansion and contraction may be noticed from time to time and these noises will dissipate with time. Please consult manufacturer prior to cleaning.

Frame Finish Options:

Paint supplied will be in-house air dry enamel. Standard colors include: dark bronze, white, black. Unlimited non-standard colors are available upon request. Anodizing is available in light, medium dark bronze, or clear. Other anodize colors quoted on request.

Standard Product Warranty:

Birdview Skylights' products are warranted to the original purchaser for a period of five years from date of shipment against defects in material or workmanship, provided that such products are installed in accordance with Birdview Skylights' installation instructions. The liability of Birdview Skylights under this warranty shall not exceed the original purchase price of the defective unit exclusive of shipping expense and installation cost. This warranty is voided if the purchaser makes any alteration to the structure of finish of the product. Birdview Skylights reserves the right to replace or repair the unit at its option. To make a claim, contact your supplier with a written statement of the defect encountered. On all claims, Birdview Skylights reserves the right to visually inspect the product and its installation. This warranty gives you specific legal rights. You may also have other rights which vary from state to state. This is a manufacturers warranty made by Birdview Skylights, Fort Worth, Texas. Extended Warranty - available upon request to meet specific project requirements.

Birdview Skylights reserves the right to discontinue or change any product without prior notice. Drawings on this website are not to scale. Please consult manufacturer for scaled drawings.